## Slide 1: Improvement in the estimation of troposphere zenith delays using high-accuracy clocks
K. Wang1),2), M. Rothacher1), M. Meindl1), E. Schoenemann3), W. Enderle3)
Institute of Geodesy and Photogrammetry, ETH Zurich, Switzerland
GNSS Research Centre, Curtin University, Australia
ESA/ESOC, Navigation Support Office, Darmstadt, Germany

## Slide 2: Overview
Introduction: clock modeling and kinematic height estimation
Motivation for this study
Results without and with clock modeling:
  Influence on kinematic heights
  Influence on zenith path delays (ZPD)
Comparison with meteo and WVR data (CEBR and ONSA)
Conclusions

## Slide 3: Highly accurate clocks (H-masers) Clock quality of some selected IGS stations
Standard deviation of clock estimates after removing a linear polynomial over one day
Standard deviation of epoch-to-epoch clock differences after removing a linear polynomial.
Standard deviations of the order of 30-120 ps (1 - 4 cm)
The epoch-to-epoch repeatability is on the level of 10 - 20 ps (3 - 6 mm, phase noise)
Indication of the size of the constraints for the clocks
Station | (in ps) | (in ps)
CEBR | 86 | 19
HERS | 30 | 13
HRAO | 39 | 11
MGUE | 27 | 10
PTBB | 114 | 12
ZECK | 30 | 11
Station |  | 
CEBR | 86 | 19
HERS | 30 | 13
HRAO | 39 | 11
MGUE | 27 | 10
PTBB | 114 | 12
ZECK | 30 | 11
August 8, 2015

## Slide 4: Highly accurate clocks Clock model
Clocks are modelled with offset , drift and a stochastic parameter
Relative constraints may be imposed on the stochastic parameter
Very weak absolute constraints are imposed for regularization

## Slide 5: Motivation Kinematic station height with clock model
Standard deviation of kinematic heights without () and with best clock model ()
Station | (in cm) | (in cm) | Improvement
CEBR | 8 | 4 | 2.0
HERS | 9 | 4 | 2.3
HRAO | 49 | 14 | 3.5
MGUE | 12 | 5 | 2.4
PTBB | 10 | 4 | 2.5
ZECK | 9 | 3 | 3.0
Station |  |  | Improvement
CEBR | 8 | 4 | 2.0
HERS | 9 | 4 | 2.3
HRAO | 49 | 14 | 3.5
MGUE | 12 | 5 | 2.4
PTBB | 10 | 4 | 2.5
ZECK | 9 | 3 | 3.0
PTBB
?
ZPD sampling of 2 hours
~ τ-1 : flicker noise

## Slide 6: Motivation Correlation of troposphere, station clock, and height
Station clock
Station height
Troposphere

## Slide 7: Kinematic station height: varying the ZPD resolution
No clock model
Clock model with 1 mm constraint
PTBB
PTBB

## Slide 8: Kinematic station height: varying the ZPD resolution
CEBR
CEBR
No clock model
Clock model with 1 mm constraint

## Slide 9: Kinematic station height: varying the ZPD resolution
Aug 2015 without (solid) and with (dashed) clock model Nov 2015
PTBB
PTBB

## Slide 10: Kinematic station height: varying the ZPD resolution
Aug 2015 without (solid) and with (dashed) clock model Nov 2015
CEBR
CEBR

## Slide 11: ZPD comparison with meteo data
STDs of the differen-ces ZPD(GPS) – ZPD (meteo)
ZPD(meteo) are free from correlations with the heights and the clocks
 Significant improve-ment in the ZPD stability, especially for high sampling rates
August 9, 2015
CEBR
HERS
HRAO
MGUE
PTBB
ZECK
Without clock modeling
With clock modeling

## Slide 12: ZPD comparison with WVR, station CEBR
Comparison of ZPD from GPS and ZPD computed from IWV data (15 min samp.)
Nov 2015
Aug 2015

## Slide 13: ZPD comparison with WVR, station CEBR, 2 days
Accuracy: comparison of ZPD from GPS with/without clock model
Reduction of the ZPD RMS when applying the clock modeling
Higher reduction at high sampling rate for the ZPD estimates
 Significant improvement of ZPD with clock modeling
15 min
2 hours
[mm]

## Slide 14: ZWD comparison with WVR, station ONSA, 5 days
Comparison of ZWD (zenith wet delay) from GPS with/without clock model and ZWD from WVR data (15 min sampling of ZWD, May 20-24, 2014)
 Much increased stability
May 2014

## Slide 15: ZWD comparison with WVR, station ONSA, 5 days
RMS of difference between ZWD from WVR data and from GPS
 All solutions imptrove with clock modeling

## Slide 16: Conclusions
Clock modeling not only improves kinematic heights but also ZPDs
With clock modeling there is no degradation in ZPDs, even for time resolution for ZPDs of 15 minutes
Comparison with meteo and WVR data (CEBR and ONSA)  improved ZWD for all solutions, when modeling the station clock
Next step: verification with a much larger data sets